## Slide 1
ECE 268 – Security of Hardware Embedded Systems
GPU Modular Arithmetic Unit
with Barrett Reduction
ECE 268 Final Project · June 2026
Akhil Teja Chirra · Vagda Sameera Talari · Abhijit Gupta
Instructor: Prof. Farinaz Koushanfar
ECE 268 – Spring 2026
Security of Hardware Embedded Systems
Notes: SPEAKER: Akhil Teja Chirra (slides 1–3) Welcome everyone. Our project implements a GPU Modular Arithmetic Unit with Barrett Reduction for ECE 268 — the Modular Arithmetic Unit track. We built a prime-agnostic modular arithmetic engine from scratch in pure CUDA and applied it to the Number Theoretic Transform, the core of post-quantum cryptography schemes like Kyber and Dilithium. I'll walk through the motivation and implementation. Sameera will cover the code and validation, and Abhijit will close with results and analysis.

## Slide 2
Motivation & Background
ECE 268 – Spring 2026
Security of Hardware Embedded Systems
Why Barrett reduction on a GPU?
1.
Integer division is slow and data-dependent on GPUs — a timing side-channel risk in crypto.
2.
Barrett replaces x mod p with multiplies + a shift using precomputed μ = ⌊2ᵏ/p⌋. No division.
3.
μ is shared across all threads (constant cache). Zero per-thread overhead, warp-uniform.
4.
__umul64hi on sm_75 is a single hardware instruction — the hot path is two multiplies.
Application: Number Theoretic Transform
a0
A0
a1
A1
a2
A2
a3
A3
Stage 1
Stage 2
Each butterfly = 2 modmuls
Used in Kyber/Dilithium (NIST PQC) and ZK-proof systems (Plonky2)
Notes: SPEAKER: Akhil Teja Chirra Why Barrett? GPU integer division is slow and data-dependent — a timing side-channel risk. Barrett turns x mod p into multiplies and a shift using a precomputed constant μ. That μ lives in constant cache, shared by all threads. On the T4, the 64-bit high-half multiply maps to a single hardware instruction __umul64hi. We chose the NTT as our crypto application because it's the core of post-quantum crypto — Kyber and Dilithium — and ZK-proofs. The butterfly structure on the right is massively parallel, and each butterfly needs exactly two modular multiplications, so NTT throughput tracks modmul throughput directly.

## Slide 3
Implementation
ECE 268 – Spring 2026
Security of Hardware Embedded Systems
Prime fields
P32
998244353 = 119·2²³+1
30-bit · Primary — NTT benchmark
P64
2⁶⁴ − 2³² + 1 (Goldilocks)
64-bit · Bonus — batch modexp / ZK
Key design: same modarith.cuh header marked __host__ __device__ compiles for both CPU (local testing, no GPU needed) and GPU (T4). Validated 2M+ random test cases locally before any GPU kernel ran.
System stack
oracle.py
Python / sympy — ground truth
host_test.cpp
CPU C++ — correctness, no GPU
modarith.cuh
__host__ __device__ Barrett · modmul · modexp
ntt.cu / bench.cu
CUDA kernels
NVIDIA T4 (sm_75)
2560 CUDA cores · Colab
Notes: SPEAKER: Akhil Teja Chirra We use two prime fields. P32 — 998244353 — is our primary NTT prime: 30-bit, NTT-friendly with 2-adicity 23. P64 — the Goldilocks prime — is used in real ZK-proof systems and is our bonus large-prime path. The system stack on the right shows the key architectural decision: modarith.cuh is marked __host__ __device__ so the same Barrett and modmul logic compiles for both CPU and GPU. We validated everything locally on a Mac with no CUDA before ever compiling a .cu file. The oracle.py Python ground-truth layer is fully independent.

## Slide 4
Code — Barrett Core (modarith.cuh)
ECE 268 – Spring 2026
Security of Hardware Embedded Systems
barrett_reduce32 — CPU/GPU shared path
// mu = floor(2^62 / P32) — precomputed once
__host__ __device__
static inline u64 barrett_reduce32(
u64 x, const Barrett32& B) {
// estimate q = floor(x/p), off by ≤1
u64 q = ((__uint128_t)x * B.mu)
>> B.shift;
u64 r = x - q * B.p; // r in [0,2p)
if (r >= B.p) r -= B.p; // correction
return r;
}
3 ops total: mul-high · mul-sub · 1 conditional sub
modmul_device — GPU-optimized path
// CPU: standard path
__host__ __device__
static inline u64 modmul(
u64 a, u64 b, const Barrett32& B){
return barrett_reduce32(a*b, B);
}
// GPU: __umul64hi = 1 asm instruction
__device__
static inline u64 modmul_device(
u64 a, u64 b, const Barrett64& B){
u64 hi = __umul64hi(a, b); // ← asm
u64 lo = a * b;
return barrett64_reduce(hi,lo,B);
}
__umul64hi = single sm_75 instruction · warp uniform
Same header, same logic — compiles for both CPU and GPU. 2M+ random cases validated locally before any GPU kernel ran.
Notes: SPEAKER: Vagda Sameera Talari (slides 4–6) barrett_reduce32 on the left is the core. Three operations: estimate q using precomputed μ and a right shift; compute residual r which lands in [0,2p); one conditional subtraction to bring r into [0,p). Zero divisions. The GPU path on the right uses __umul64hi — a single hardware instruction on sm_75 that computes the high 64 bits of a 128-bit product. Two multiplies total, completely warp-uniform. The key point at the bottom: same code compiles for both. We ran 2 million random test cases against Python/sympy ground truth on the CPU before ever compiling a CUDA file.

## Slide 5
Code — GPU NTT Kernel (ntt.cu)
ECE 268 – Spring 2026
Security of Hardware Embedded Systems
ntt_stage_kernel — one thread per butterfly pair
__global__ void ntt_stage_kernel(
u64* A, int n, int half,
u64 w, const Barrett32 B) {
int tid = blockIdx.x*blockDim.x + threadIdx.x;
if (tid >= n/2) return;
int j = tid % half;
int u_i = (tid/half)*2*half + j;
int v_i = u_i + half;
// Cooley-Tukey butterfly
u64 tw = modpow_device(w, j, B);
u64 u = A[u_i];
u64 v = modmul_device(A[v_i], tw, B); // Barrett
A[u_i] = modadd(u, v, B.p);
A[v_i] = modsub(u, v, B.p);
}
// launched log₂n times, n/2 threads each
Design choices
Per-stage launch
log₂n separate kernel calls, n/2 threads each. Global sync at kernel boundary keeps it simple and correct.
In-place Cooley-Tukey
Single contiguous buffer. Bit-reversal permutation kernel runs once before the forward transform.
Barrett over Montgomery
Data stays in normal residue form across all stages — avoids two extra O(n) domain-conversion passes that would hurt memory bandwidth at large n.
Dual __host__ __device__
Same butterfly arithmetic runs on both CPU and T4. Triple-verified: GPU ≡ CPU ≡ Python.
Notes: SPEAKER: Vagda Sameera Talari One CUDA thread handles one butterfly pair. The index arithmetic at lines 9-10 maps thread ID to the right u and v elements. The highlighted lines are the actual computation — one modmul, one modadd, one modsub. Four design decisions on the right. Per-stage launches give us implicit global sync at kernel boundaries — simpler than shared-memory coordination. In-place Cooley-Tukey avoids extra allocation. Barrett over Montgomery is the most important choice: data stays in natural form across all stages, so we avoid two O(n) passes over device memory that Montgomery would require. And the dual compilation means the same butterfly arithmetic is triple-verified before the GPU ever runs it.

## Slide 6
Correctness & Validation
ECE 268 – Spring 2026
Security of Hardware Embedded Systems
Three-layer verification: GPU (nvcc) ≡ CPU C++ (clang) ≡ Python/sympy
Test
Count
Result
Barrett32 / Barrett64 — 2M+ random + boundary operands
2M+ each
0 failures
modexp / modinv (P32 & P64) — random exponents
100K
0 failures
NTT round-trip: INTT(NTT(x)) == x (CPU)
n ≤ 2¹⁴
pass
NTT convolution vs. naive O(n²) (CPU)
n ≤ 2⁹
pass
GPU NTT matches CPU output element-wise
2⁴ – 2²⁰
pass
Batch modexp P64 — 1M independent (GPU vs CPU)
1,048,576
0 mismatches
Notes: SPEAKER: Vagda Sameera Talari We enforced a three-layer protocol: GPU output must equal CPU C++ must equal Python sympy. Running through the table: 2 million random and boundary cases for Barrett on both primes — zero failures. 100K random exponents for modexp and modinv — zero failures. NTT round-trip and convolution pass on the CPU. GPU NTT matches CPU element-wise for every size 2^4 through 2^20. And 1,048,576 independent batch modexp over the Goldilocks prime — zero mismatches. The three-layer check matters because a GPU bug and a CPU bug could in theory agree on a wrong answer. The independent Python/sympy layer using arbitrary-precision integers closes that loop. Handing over to Abhijit for results.

## Slide 7
Performance Results — NVIDIA T4 (sm_75, Colab)
ECE 268 – Spring 2026
Security of Hardware Embedded Systems
NTT kernel speedup vs array size
10×
20×
30×
40×
52×
2¹⁰
2¹²
2¹⁴
2¹⁶
2¹⁸
peak
52×
2²⁰
2²²
n
GPU < CPU at n=2¹⁰ — kernel launch overhead not yet amortized. Peak 52× at n=2¹⁸ — working set fits in T4 L2. Above 2¹⁸: memory-bandwidth-bound, speedup dips.
Summary of measured speedups
Barrett modmul (n=4M)
569×
131 Gops/s vs 0.23 Gops/s
NTT kernel peak (n=2¹⁸)
52×
0.367 ms GPU vs 19.0 ms CPU
NTT end-to-end (n=2²²)
19×
incl. PCIe transfer
Batch modexp P64 (1M)
277×
3.4 ms GPU vs 955 ms CPU
Notes: SPEAKER: Abhijit Gupta (slides 7–9) The bar chart shows NTT kernel speedup across array sizes. The important story is the shape: GPU is actually slower than a single CPU core at n=2^10 — kernel launch overhead hasn't been amortized yet. It breaks even around n=2^12 and peaks at 52× at n=2^18, where the working set fits in T4's L2 cache. Above that, the kernel becomes memory-bandwidth-bound and speedup dips to 35-40×. The table on the right gives the headline numbers. Barrett modmul is 569× — that's embarrassingly parallel, no inter-thread communication. Batch Goldilocks modexp hits 277× on 1M elements with zero mismatches. End-to-end NTT including PCIe transfer peaks around 19× at large n.

## Slide 8
Analysis
ECE 268 – Spring 2026
Security of Hardware Embedded Systems
Barrett vs. Montgomery for NTT
Domain
→ natural residue — no conversion
Montgomery domain (in/out passes needed)
NTT stages
→ data stays in natural form throughout
two extra O(n) passes (convert in, convert out)
Per reduction
→ mul-high + mul-sub + 1 cond. sub
similar, but conversion cost amortized
Winner for NTT
→ Barrett — saves 2 memory BW passes
At large n the NTT is memory-bandwidth-bound. Montgomery would add two full O(n) scans over device memory — exactly the wrong trade-off.
Performance vs. security
Timing side channel in modexp
square-and-multiply branches on exponent bits. If the exponent is secret (RSA private key), this leaks timing information. Fix: Montgomery ladder.
Data-dependent Barrett correction
if (r >= p) r -= p leaks one residual bit. Branch-free fix: r -= p & -(u64)(r >= p). Cost: negligible.
Field size vs. throughput
P32 (30-bit): 569×. P64 (64-bit): 277×. RSA-2048 would need multi-limb arithmetic — much lower throughput. Security margin costs compute.
Batch model and attacker advantage
277× on 1M independent exponentiations also means GPU accelerates parallel brute-force. A single RSA-2048 decryption is sequential — GPU advantage requires batching.
Notes: SPEAKER: Abhijit Gupta On the left, Barrett versus Montgomery. Montgomery can save an operation per reduction in tight loops, but for NTT it requires two extra O(n) passes over device memory — converting into Montgomery domain before the transform and back out after. At large n where the NTT is already memory-bandwidth-bound, those two passes would materially reduce speedup. Barrett keeps data in natural form across all butterfly stages, which is exactly what we want. On the right, four security points without sugarcoating. Our modexp branches on exponent bits — that's a timing side channel. The Barrett correction is also data-dependent. Both are easy to fix but we prioritized throughput for benchmarking. The field-size tradeoff is real: 569× on P32 drops to 277× on P64. And the batch parallelism that gives us 277× also gives an attacker the same advantage for brute-force.

## Slide 9
Conclusion
What we showed
–
Pure-CUDA Barrett engine — prime-agnostic, __host__ __device__ dual compilation
–
569× speedup for modmul (131 Gops/s vs 0.23 Gops/s single-thread CPU)
–
52× NTT peak at n=2¹⁸ — shifts compute-bound → memory-bandwidth-bound
–
277× batch Goldilocks modexp · 0 mismatches across 1M exponentiations
–
3-way correctness: GPU ≡ CPU C++ ≡ Python/sympy
Key takeaways
Dual compilation
Validate locally with 2M+ test cases before touching a GPU — saved us significant debugging time on cloud resources.
Barrett for NTT
Avoids two extra O(n) memory passes that Montgomery would need between stages. Critical when NTT is BW-bound at large n.
GPU is not free
Slower than a single CPU core at n=2¹⁰. Speedup is a function of occupancy and memory behavior, not just hardware.
github.com/achirra-cipher/ece268-gpu-modarith
ECE 268 – Spring 2026
Security of Hardware Embedded Systems
Notes: SPEAKER: Abhijit Gupta To summarize. We built a prime-agnostic GPU Barrett reduction engine in pure CUDA, validated three ways. 569× modmul speedup, 52× NTT peak, 277× batch modexp, zero correctness failures. Three takeaways worth keeping. First, the dual compilation strategy — validating 2M+ arithmetic cases locally before running any GPU kernel saved significant debugging cost on expensive cloud resources. Second, Barrett is the right choice for NTT because it avoids two O(n) domain-conversion memory passes that Montgomery would need between stages. Third, GPU speedup is not automatic — we're actually slower than a single CPU core at n=2^10. It's about occupancy and memory behavior. Full source and Colab notebook at the GitHub link. Thank you.