## Slide 1
ECE 268 – Security of Hardware Embedded Systems
GPU Modular Arithmetic Unit
with Barrett Reduction
ECE 268 Final Project · June 2026
Akhil Teja Chirra · Vagda Sameera Talari · Abhijit Gupta
Instructor: Prof. Farinaz Koushanfar
ECE 268 – Spring 2026
Security of Hardware Embedded Systems │ 1 / 9
Notes: [~30 sec] TITLE SLIDE — Akhil Teja Chirra speaking. "Good morning everyone. Our project is a GPU-accelerated modular arithmetic engine built around Barrett reduction, targeting the NVIDIA T4. We chose this because modular arithmetic — specifically modular multiplication and exponentiation — is the computational bottleneck in post-quantum cryptography and zero-knowledge proof systems. The question we set out to answer was: can we achieve meaningful speedups over a single CPU core while maintaining bit-for-bit correctness? The short answer is yes — 569x for raw modular multiply and 52x for an NTT kernel." Team: Akhil Teja Chirra, Vagda Sameera Talari, Abhijit Gupta. Instructor: Prof. Farinaz Koushanfar | ECE 268, Spring 2026. GitHub: github.com/achirra-cipher/ece268-gpu-modarith

## Slide 2
Motivation & Background
ECE 268 – Spring 2026
Security of Hardware Embedded Systems │ 2 / 9
Problem: Modular Arithmetic is the Crypto Bottleneck
1.
GPU has no native division instruction: it compiles to ~20 ops and is data-dependent — a timing side-channel in constant-time crypto.
2.
Barrett: precompute μ = ⌊2ᵏ/p⌋ once. Then x mod p ≈ x − ⌊xμ/2ᵏ⌋·p using only multiplies + shift. Constant-time friendly.
3.
μ lives in GPU constant cache — broadcast to all threads in a warp simultaneously. Zero per-thread overhead; fully warp-uniform execution.
4.
On sm_75 (T4): __umul64hi(a,b) is one IMUL.HI instruction. Full Barrett hot-path = 2 multiplies + 1 conditional subtract.
Target Application: Number Theoretic Transform (NTT)
a0
A0
a1
A1
a2
A2
a3
A3
Stage 1
Stage 2
Each butterfly = 2 modmuls → NTT throughput ∝ modmul throughput
Used in NIST PQC standards (Kyber, Dilithium) and ZK-proof systems (Plonky2, Halo2). n/2 independent butterflies per stage → massive GPU parallelism.
Notes: [~90 sec] MOTIVATION & BACKGROUND — Akhil or Vagda speaking. Opening hook: "Modular arithmetic is everywhere in cryptography — RSA, elliptic curves, post-quantum lattice schemes, and zero-knowledge proofs all reduce to the same bottleneck: x mod p, repeated billions of times." KEY POINTS TO HIT: 1. GPU integer division is SLOW and DATA-DEPENDENT. On modern GPUs there is no native integer division instruction — it compiles to a multi-instruction sequence of ~20 ops. More critically it is data-dependent, creating timing variation that is a side-channel in cryptographic settings. 2. Barrett reduction replaces division with precomputed multiplication. The formula: given mu = floor(2^k / p) precomputed once, we compute q = floor(x * mu / 2^k) using only multiplications and a right shift, then r = x - q*p. The key insight: mu is constant for a given prime p, so it lives in GPU constant cache — zero per-thread overhead. 3. The GPU instruction __umul64hi on sm_75 (T4) computes the upper 64 bits of a 128-bit product in a SINGLE hardware instruction. This maps perfectly to the Barrett algorithm. 4. We target NTT (Number Theoretic Transform) as our benchmark application because: (a) it is the inner loop of Kyber and Dilithium — the NIST-selected post-quantum standards, (b) each NTT butterfly requires exactly 2 modular multiplications, so NTT throughput directly measures modmul throughput, and (c) it is massively parallel — n/2 independent butterflies per stage. Expected question: "Why not use Montgomery reduction?" — we address this in the Analysis slide. Short answer: Barrett avoids two O(n) domain-conversion passes critical when NTT is memory-bandwidth-bound.

## Slide 3
Implementation
ECE 268 – Spring 2026
Security of Hardware Embedded Systems │ 3 / 9
Prime fields
P32
998244353 = 119·2²³+1
30-bit · Primary - NTT benchmark
P64
2⁶⁴ − 2³² + 1 (Goldilocks)
64-bit · Bonus - batch modexp / ZK
Core contribution: modarith.cuh marked __host__ __device__ compiles identically for CPU (clang++) and GPU (nvcc/T4). 2M+ random Barrett + modexp cases validated on CPU before any Colab GPU job - all algorithmic bugs caught locally.
System stack
oracle.py
Python / sympy - ground truth
host_test.cpp
CPU C++ - correctness, no GPU
modarith.cuh
__host__ __device__ Barrett · modmul · modexp
ntt.cu / bench.cu
CUDA kernels
NVIDIA T4 (sm_75)
2560 CUDA cores · Colab
Notes: [~60 sec] IMPLEMENTATION OVERVIEW — Abhijit speaking. KEY POINTS TO HIT: 1. PRIME FIELDS: We support two primes. P32 = 998244353 = 119*2^23+1 is a 30-bit NTT-friendly prime with a primitive root of 3 — the standard benchmark prime for NTT. P64 = 2^64 - 2^32 + 1 (Goldilocks) is a 64-bit prime used in ZK-proof systems like Plonky2; we use it for batch modular exponentiation. 2. CORE DESIGN DECISION — dual __host__ __device__ compilation. The same modarith.cuh header compiles for both CPU (via clang++ without any GPU) and GPU (via nvcc for T4). This was critical: we ran 2 million+ random test cases locally with zero GPU time before ever submitting a Colab job. This saved us significant debugging cycles. 3. SYSTEM STACK: Four-layer stack. Python/sympy acts as ground truth oracle. C++ host test validates the Barrett implementation on CPU. modarith.cuh contains the core Barrett/modmul/modexp logic. CUDA kernels (ntt.cu, bench.cu) run on the T4. 4. HARDWARE: NVIDIA T4 GPU on Google Colab — 2560 CUDA cores, sm_75 architecture, 16 GB GDDR6. Expected question: "Why did you validate locally first?" — Cloud GPU time is a limited resource on Colab. Local validation with 2M cases caught all our algorithmic bugs before we ever needed a T4.

## Slide 4
Code — Barrett Core (modarith.cuh)
ECE 268 – Spring 2026
Security of Hardware Embedded Systems │ 4 / 9
barrett_reduce32 - CPU/GPU shared path
// mu = floor(2^62 / P32) — precomputed once
__host__ __device__
static inline u64 barrett_reduce32(
u64 x, const Barrett32& B) {
// estimate q = floor(x/p), off by ≤1
u64 q = ((__uint128_t)x * B.mu)
>> B.shift;
u64 r = x - q * B.p; // r in [0,2p)
if (r >= B.p) r -= B.p; // correction
return r;
}
3 ops total: mul-high · mul-sub · 1 conditional sub
modmul_device - GPU-optimized path
// CPU: standard path
__host__ __device__
static inline u64 modmul(
u64 a, u64 b, const Barrett32& B){
return barrett_reduce32(a*b, B);
}
// GPU: __umul64hi = 1 asm instruction
__device__
static inline u64 modmul_device(
u64 a, u64 b, const Barrett64& B){
u64 hi = __umul64hi(a, b); // ← asm
u64 lo = a * b;
return barrett64_reduce(hi,lo,B);
}
__umul64hi = single sm_75 instruction · warp uniform
Same header, same logic - compiles for both CPU and GPU. 2M+ random cases validated locally before any GPU kernel ran.
Notes: [~90 sec] CODE — BARRETT CORE — Vagda speaking. This is the heart of the project. Walk through the code carefully. BARRETT REDUCE 32 (left panel): - mu = floor(2^62 / P32) is precomputed ONCE when the Barrett32 struct is initialized — this happens on the host and the value is passed to the GPU as a constant. - q = (x * mu) >> shift: this is the floor division estimate. The __uint128_t cast is needed on CPU. On GPU the modmul_device path uses __umul64hi to get the high half natively. - r = x - q*p: this subtraction may leave r in [0, 2p). The conditional r -= p brings it to [0, p). This is exactly one conditional subtract — branch-free versions exist (r -= p & -(uint64_t)(r >= p)) and we discuss the timing implication in the Analysis slide. - Total: 3 operations — mul-high, mul-sub, 1 conditional subtract. MODMUL DEVICE (right panel): - On CPU: just multiply a*b and call barrett_reduce32. The compiler handles 128-bit internally. - On GPU: __umul64hi(a, b) extracts the upper 64 bits of the 128-bit product a*b in a SINGLE sm_75 assembly instruction (IMUL.HI). This is warp-uniform — all threads in a warp compute the same instruction, no divergence. - The Barrett64 path for Goldilocks uses a specialized reduction exploiting the Mersenne-like structure of 2^64 - 2^32 + 1. KEY INSIGHT TO EMPHASIZE: The SAME header file compiles for both CPU and GPU. There is no duplication of logic. The __host__ __device__ annotation tells nvcc to emit two code paths: one for the host compiler, one for the GPU.

## Slide 5
Code - GPU NTT Kernel (ntt.cu)
ECE 268 – Spring 2026
Security of Hardware Embedded Systems │ 5 / 9
ntt_stage_kernel - one thread per butterfly pair
__global__ void ntt_stage_kernel(
u64* A, int n, int half,
u64 w, const Barrett32 B) {
int tid = blockIdx.x*blockDim.x + threadIdx.x;
if (tid >= n/2) return;
int j = tid % half;
int u_i = (tid/half)*2*half + j;
int v_i = u_i + half;
// Cooley-Tukey butterfly
u64 tw = modpow_device(w, j, B);
u64 u = A[u_i];
u64 v = modmul_device(A[v_i], tw, B); // Barrett
A[u_i] = modadd(u, v, B.p);
A[v_i] = modsub(u, v, B.p);
}
// launched log₂n times, n/2 threads each
Design choices
Per-stage launch
log₂n separate kernel calls, n/2 threads each. Global sync at kernel boundary keeps it simple and correct.
In-place Cooley-Tukey
Single contiguous buffer. Bit-reversal permutation kernel runs once before the forward transform.
Barrett over Montgomery
Data stays in normal residue form across all stages - avoids two extra O(n) domain-conversion passes that would hurt memory bandwidth at large n.
Dual __host__ __device__
Same butterfly arithmetic runs on both CPU and T4. Triple-verified: GPU ≡ CPU ≡ Python.
Notes: [~90 sec] CODE — GPU NTT KERNEL — Akhil speaking. Walk through the kernel carefully. NTT_STAGE_KERNEL: - One thread per butterfly pair. Thread tid handles the butterfly at positions u_i and v_i. - The kernel is launched log2(n) times with n/2 threads each. Each launch is one NTT stage. Global synchronization happens at the kernel boundary — the GPU completes all threads before the next kernel starts. This is simpler and more correct than shared-memory synchronization. COOLEY-TUKEY BUTTERFLY: - tw = modpow_device(w, j, B) computes the twiddle factor — the j-th power of the primitive root w. This is per-thread but precomputing a twiddle table would improve performance further (mentioned as future work). - A[u_i] = u + v (mod p), A[v_i] = u - v (mod p) — both using Barrett modadd/modsub. - In-place: single contiguous buffer, no extra memory allocation. Bit-reversal permutation runs once before the forward NTT. DESIGN CHOICES (right panel) — explain each: 1. Per-stage launch: log2(n) kernel calls. Global sync at boundary. Simple and provably correct. 2. In-place Cooley-Tukey: memory efficient, single buffer. 3. Barrett over Montgomery: data stays in natural (non-Montgomery) residue form throughout all NTT stages. Montgomery would require converting the entire array into Montgomery domain before NTT and converting back after — two extra O(n) memory passes. At large n where NTT is bandwidth-bound, this is expensive. 4. Dual __host__ __device__: same butterfly arithmetic on both CPU and T4 — triple-verified correctness. Expected question: "Did you try shared memory tiling?" — No, due to time constraints. It would improve cache efficiency for larger n.

## Slide 6
Correctness & Validation
ECE 268 – Spring 2026
Security of Hardware Embedded Systems │ 6 / 9
Three-layer verification: GPU (nvcc) ≡ CPU C++ (clang) ≡ Python/sympy
Test
Count
Result
Barrett32 / Barrett64 - 2M+ random + boundary operands
2M+ each
0 failures
modexp / modinv (P32 & P64) - random exponents
100K
0 failures
NTT round-trip: INTT(NTT(x)) == x (CPU)
n ≤ 2¹⁴
pass
NTT convolution vs. naive O(n²) (CPU)
n ≤ 2⁹
pass
GPU NTT matches CPU output element-wise
2⁴ – 2²⁰
pass
Batch modexp P64 - 1M independent (GPU vs CPU)
1,048,576
0 mismatches
Notes: [~60 sec] CORRECTNESS & VALIDATION — Abhijit speaking. "Before showing performance numbers, let me establish that all numbers are correct." THREE-LAYER VERIFICATION STRATEGY: - Layer 1: Python/sympy — arbitrary-precision oracle, no rounding, guaranteed correct. Every operation result is checked against Python. - Layer 2: CPU C++ — host_test.cpp validates the Barrett logic without any GPU. If the CPU C++ matches Python, our algorithm is correct; any GPU discrepancy is then a CUDA implementation bug, not an algorithmic bug. - Layer 3: GPU — ntt.cu output compared element-wise against CPU output. TABLE WALKTHROUGH: - Barrett32/64: 2 million+ random operands plus all boundary cases (0, 1, p-1, p-2, 2p-1). Zero failures. - modexp/modinv: 100K random exponents. Zero failures. - NTT round-trip: INTT(NTT(x)) == x for all n up to 2^14. Pass. This validates both forward and inverse transform. - NTT convolution: GPU NTT-based polynomial multiply matches naive O(n^2) reference. Pass. - GPU vs CPU element-wise: n from 16 to 1M (2^4 to 2^20). Pass. - Batch modexp P64: 1,048,576 independent exponentiations — 0 mismatches. KEY MESSAGE: "We did not present a single performance number until we had validated correctness across all these cases. Performance without correctness is meaningless in a cryptographic context."

## Slide 7
Performance Results — NVIDIA T4 (sm_75, Colab)
ECE 268 – Spring 2026
Security of Hardware Embedded Systems │ 7 / 9
NTT kernel speedup vs array size
10×
20×
30×
40×
52×
2¹⁰
2¹²
2¹⁴
2¹⁶
2¹⁸
peak
52×
2²⁰
2²²
n
n=2¹⁰: GPU slower than CPU - kernel launch overhead dominates 512-thread workload. n=2¹⁸: 52× peak - 262K elements (2 MB) fit in T4 L2 cache (4 MB), full occupancy. n>2¹⁸: memory-bandwidth-bound, speedup decreases to 19× end-to-end at n=2²² (includes PCIe transfer).
Summary of measured speedups
Barrett modmul (n=4M)
569×
131 Gops/s vs 0.23 Gops/s
NTT kernel peak (n=2¹⁸)
52×
0.367 ms GPU vs 19.0 ms CPU
NTT end-to-end (n=2²²)
19×
incl. PCIe transfer
Batch modexp P64 (1M)
277×
3.4 ms GPU vs 955 ms CPU
Notes: [~90 sec] PERFORMANCE RESULTS — Vagda speaking. This slide has two parts: the NTT speedup chart and the summary table. NTT SPEEDUP CHART — walk through each region: - n = 2^10 (1024): GPU is SLOWER than CPU. The kernel launch overhead (~5-10 microseconds) dominates when only 512 threads run for a handful of stages. This is expected — GPU only wins at sufficient parallelism. - n = 2^12 to 2^16: Speedup rises steeply. More threads → better occupancy → launch overhead amortized. - n = 2^18 (262,144): PEAK SPEEDUP of 52x. The working set (2MB for 64-bit elements) fits in T4's 4MB L2 cache. This is the sweet spot: enough parallelism for full occupancy, data still in cache. - n = 2^20 to 2^22: Speedup drops from 52x to ~19x end-to-end (including PCIe transfer). The array no longer fits in L2 — kernel becomes memory-bandwidth-bound. GPU memory bandwidth (300 GB/s) still beats CPU cache bandwidth, but the advantage narrows. SUMMARY TABLE: - Barrett modmul (4M elements): 569x — 131 billion operations/second on GPU vs 0.23 Gops/s single-thread CPU. This is the raw arithmetic throughput number. - NTT kernel peak: 52x — 0.367ms GPU vs 19.0ms CPU for n=2^18. - NTT end-to-end including PCIe data transfer: 19x at n=2^22. - Batch modexp Goldilocks (1M independent): 277x — 3.4ms GPU vs 955ms CPU. INTERPRETATION: "The 569x raw modmul speedup reflects pure compute parallelism with no memory bottleneck. The NTT speedup is lower because NTT is partially memory-bandwidth-bound at large n. The end-to-end 19x still includes PCIe overhead — for in-GPU pipelines the speedup is closer to 52x."

## Slide 8
Analysis
ECE 268 – Spring 2026
Security of Hardware Embedded Systems │ 8 / 9
Barrett vs. Montgomery for NTT
Domain
→ Barrett: natural residue throughout - no domain conversion
Montgomery: requires full O(n) domain-in + domain-out passes
NTT stages
→ data stays in natural form throughout
two extra O(n) passes (convert in, convert out)
Per reduction
→ mul-high + mul-sub + 1 cond. sub
similar, but conversion cost amortized
Winner for NTT
→ Barrett - saves 2 memory BW passes
At large n the NTT is memory-bandwidth-bound. Montgomery would add two full O(n) scans over device memory - exactly the wrong trade-off.
Performance vs. security
Timing side channel in modexp
Standard square-and-multiply leaks exponent bits via timing. Fix: Montgomery ladder (constant-time, always does both square and multiply). Relevant if GPU is used for RSA private-key operations.
Data-dependent Barrett correction
if (r >= p) r -= p is data-dependent - leaks one bit. Branch-free: r -= p & -(u64)(r >= p). Cost negligible; should be used in constant-time contexts.
Field size vs. throughput
P32 (30-bit): 569×. P64 (64-bit): 277×. RSA-2048 would need multi-limb arithmetic - much lower throughput. Security margin costs compute.
Batch model and attacker advantage
277× on 1M independent exponentiations also means GPU accelerates parallel brute-force. A single RSA-2048 decryption is sequential - GPU advantage requires batching.
Notes: [~90 sec] ANALYSIS — Akhil speaking. Two analysis sections: Barrett vs Montgomery, and Performance vs Security. BARRETT VS MONTGOMERY FOR NTT: - Montgomery reduction requires data to be in "Montgomery domain" — multiply by R mod p before computation, divide by R mod p after. For a single modmul this is fine; the conversion cost amortizes. - For NTT with log2(n) stages: ALL n elements must be converted INTO Montgomery domain before stage 1, and ALL n elements converted OUT after the last stage. That's two extra full O(n) memory passes. - At n=2^20, each pass reads/writes 8MB of data. On the T4 with 300 GB/s memory bandwidth, each extra pass costs ~26 microseconds. Two passes = ~52 microseconds wasted per NTT. - At large n the NTT is already memory-bandwidth-bound. Montgomery adds exactly the wrong overhead. - WINNER: Barrett — data stays in natural residue form throughout. PERFORMANCE VS SECURITY: 1. Timing side channel in modexp: standard square-and-multiply leaks which bits of the exponent are 1 (square-then-multiply takes longer than square-only). Fix: Montgomery ladder — always does both square and multiply. We did not implement this — it is future work. 2. Data-dependent Barrett correction: the "if (r >= p) r -= p" branch leaks one bit of information per reduction. Branch-free fix: r -= p & -(uint64_t)(r >= p). Cost is negligible. We discuss this as a known issue. 3. Field size vs throughput: P32 gives 569x, P64 gives 277x. RSA-2048 needs 2048-bit multi-limb arithmetic — much slower. Security margin directly costs compute. 4. Batch model: 277x on 1M independent exponentiations also means an adversary with GPU access can accelerate brute-force attacks. Context matters. KEY MESSAGE: "Performance and security are in tension. Our implementation optimizes throughput, but a production system would need Montgomery ladder for secret-key exponentiation."

## Slide 9
Conclusion
What we showed
–
Pure-CUDA Barrett engine - prime-agnostic, __host__ __device__ dual compilation
–
569× speedup for modmul (131 Gops/s vs 0.23 Gops/s single-thread CPU)
–
52× NTT peak at n=2¹⁸ - shifts compute-bound → memory-bandwidth-bound
–
277× batch Goldilocks modexp · 0 mismatches across 1M exponentiations
–
3-way correctness: GPU ≡ CPU C++ ≡ Python/sympy
Key takeaways
Dual compilation
2M+ CPU test cases before any GPU job. All algorithmic bugs caught locally, zero wasted Colab GPU hours.
Barrett for NTT
Saves 2 full O(n) memory passes vs. Montgomery. At n=2²⁰ (GDDR6 at 300 GB/s) this is ~52μs - significant when NTT is bandwidth-bound.
GPU is not free
GPU loses at n=2¹⁰ (kernel launch overhead > compute). Speedup requires sufficient parallelism + data to amortize launch cost.
github.com/achirra-cipher/ece268-gpu-modarith
ECE 268 – Spring 2026
Security of Hardware Embedded Systems │ 9 / 9
Notes: [~60 sec] CONCLUSION — Abhijit speaking. WHAT WE SHOWED (tick through each): 1. Pure-CUDA Barrett engine: prime-agnostic, __host__ __device__ dual compilation — same code runs on CPU and GPU. 2. 569x speedup for raw Barrett modmul: 131 Gops/s GPU vs 0.23 Gops/s single-thread CPU. 3. 52x NTT kernel peak at n=2^18 — working set fits L2 cache. Above 2^18: transitions from compute-bound to memory-bandwidth-bound. 4. 277x batch Goldilocks modexp for 1M independent exponentiations — 0 mismatches. 5. 3-way correctness: GPU == CPU C++ == Python/sympy across all test cases. THREE KEY TAKEAWAYS: 1. Validate locally first: 2M+ CPU test cases before any GPU kernel. Saves cloud GPU hours and speeds debugging. 2. Barrett beats Montgomery for NTT: avoids two extra O(n) memory passes. Critical when NTT is bandwidth-bound at large n. 3. GPU speedup is not free: slower than CPU at n=2^10. Speedup is a function of occupancy, memory behavior, and amortized launch overhead — not just hardware parallelism. FUTURE WORK (if asked): - Precomputed twiddle factor tables to avoid per-thread modpow in NTT kernel. - Shared-memory tiling for better L1 utilization. - Montgomery ladder for constant-time modexp. - Mixed-radix NTT for non-power-of-2 sizes. GITHUB: github.com/achirra-cipher/ece268-gpu-modarith — full history, all contributions labeled by team member.